## Slide 1: Nameplate Capacity
300.000 t/y ( feed gasoil)
260.000 t/y (feed VN IQ120)
(1 compression line)
(822 t/d x 365 d/y)

## Slide 2: Energetic Index
7200 Kcal/Kg ethylene
(1 compression line)

## Slide 3: Furnaces
N° 4 Selas furnaces duty 43x106 Kcal/h
N° 5 Foster Wheeler furnaces duty 15x106 Kcal/h
N° 2 Foster Wheeler Ethane recycle furnaces duty15x106 Kcal/h.

## Slide 4: Feedstocks
Gasoil 32%
Virgin Naphta 54%
Raffinate 13%
LPG
C5 Aromatics cut 1%
Condensate on availability

## Slide 5: Charge Gas Compressor
Compressor C1 Electric Driver 14 MWatt 260.000 t/y of ethylene
Compressor C6 Turbine driver 14 MWatt 186.000 t/y ethylene

## Slide 6: Medium temperature Section
Light ends Splitter column 1500 days reboiler 200 days
Depropanation column column 1000 days
reboiler 200 days
Caustic Tower Caustic concentration 4% Caustic consumption 2 Kg/t ethylene

## Slide 7: Cold Section
Ethylene Splitter
Start up 1986 capacity 300.000 t/y of ethylene
Acethylene Reactors Sud Chemie catalyst G58C Start up 2006 Inlet T 50°C I e 60°C II End of run T 60°C I e 70°C II regeneration cycle 210 days molar ratio 1,1 I e 1,7 II
MAPD Reactors catalyst CCI C-31 inlet T 75°C regeneration cycle 4 years Catalyst life 28 years

## Slide 8: Ethylene chilling cycle
Compressor C3 turbine driver
Compressor C8 electric driver 3,5 MWatt

## Slide 9: Chilling cycle with propylene
Compressor C2 backpressure turbine The backpressure turbine CT-2A has a power of 9 Mwatt and is suitable to one compression line run
Compressor C7 condensing turbine CT-7 turbine has a power of 10,5 Mwatt and is suitable to two compression lines run